## Slide 1: The use of DST for Bellaterra university case
2nd DECISIVE Webinar - The DST
11st June 2021, on-line
Fundació ENT
Rosaria Chifari

## Slide 2: AGENDA
Objective
Baseline/Alternative scenario diagrams
Waste process libraries to build
Data needed for the DST
Data gathering steps
….
….

## Slide 3: Objective
Building scenarios for the Bellaterra University Campus in the DST to compare results
“INNOVATIVE” SCENARIO
DECISIVE systems
(mAD+ Stirling motor)
“BASELINE” SCENARIO
Centralized biowaste management system
Dentralized biowaste management system

## Slide 4
Bellaterra Waste management system: Baseline
MSW
Biostabilization
FINAL DESTINATION
Incineration
Landfill
Waste Water treatment
Bring scheme
BIOWASTE
RESIDUAL WASTE
Mechanical separation
Bring scheme
Post-Composting
Digestate
Maturation
Agriculture
Compost
Refuse
Recycling
RECYCLABLES
234
487
47
197 t/y
570 t/y
CHP
Thermal Energy
Electricity
Refuse
Refuse
Refuse
Mechanical separation
Source Separation
Anaerobic Digestion
GENERATION
COLLECTION
SOURCE SEPARATION
PRE TREATMENT
TREATMENT
Biogas
Baseline scenario diagram
TRANSPORT
10 Restaurants in UAB University
UAB
University residence

## Slide 5
Bellaterra Waste management system: Baseline
MSW
10 Restaurants in UAB University
UAB
University residence
Biostabilization
FINAL DESTINATION
Incineration
Landfill
Waste Water treatment
Door to Door
BIOWASTE
RESIDUAL WASTE
Hygienization
Door to
Door
Digestate
Maturation
Agriculture
Compost
Refuse
Recycling
RECYCLABLES
234
432
103
197 t/y
570 t/y
Stirling
Thermal Energy
Electricity
Refuse
Mechanical separation
Source Separation
Micro AD
GENERATION
COLLECTION
SOURCE SEPARATION
PRE TREATMENT
TREATMENT
Biogas
Alternative scenario diagram
TRANSPORT
increase in SS BW
change in collection system
decrease in SS BW
unvaried recyclables
Liquid digestate

## Slide 6: Building inventories in the DST
To build scenarios we need to building Data /Inventories for the waste processes
Understanding which data we will need for the inventories in the DST
Looking for the available data
Introducing data/inventories in the DST

## Slide 7: Which data are needed?
For each stage of the biowaste management system a list of data/ indicators will be needed for building inventories/libraries in the DST
Phases of BWMS in the DST

## Slide 8: Generation
Source size
Biowaste generation (t/unit)
Type of source
Waste type
Generation Unit
Composition Biowaste (%)
Food Waste Composition
Notes: Biowaste sources:
Type of Source (Household, Restaurant, Student residence, Hospital etc.)
Waste type (Biowaste, Source separated biowaste, Residual waste, Municipal Solid Waste, Other)
Generation Unit: it represents the unit of generation of biowaste. it can be: person, meal, bed, etc.
Mass flow parameters:
Source size (generation unit/year): it is the number of generation units (number of residents).
Biowaste Generation Amount (t/unit): amount of biowaste generated per Generation Unit.
Biowaste Composition: % of food waste, green waste, woody waste and other organic waste in the biowaste represented in this process.
Food waste Composition: % of avoidable and unavoidable FW

## Slide 9: Source Separation
Waste Outputs:
SSBW
RW
Mass Flow Parameters
% Macro-impurities in SSBW
Macro-impurities Composition (%)
Material inputs
Socio-economic aspects
Mass distribution of the FW, GW, WW in RW and SSBW
Consumption of Bags, Buckets, Containers
Public and private space occupation,
Private generator time
Notes: Waste Outputs. i.e. the biowaste generated in a source is separated in two streams: Source-Separated Biowaste (SSBW) and Residual Waste (RW)
Content of macro-impurities in the SSBW (in wet weight) and the Composition of such macro-impurities (glass, paper& cardboard, plastic, ferrous non Ferrous and other)
Material inputs: Amount of bags and or buckets, Amount of containers, Socio–economic aspects

## Slide 10: Collection
Type of Collection
Inventories per tonne*km
the unit impacts of such inventories are later multiplied by the tonnes of waste times the distance along which the waste is transferred.
Consumption
Trucks
Diesel
Material and energy inputs
Socio-economic aspects
Worker
Public space
Notes: the gathering of the waste from the different collection points and its transference to the waste facility collection process mainly includes trucks, combustible and labour associated with the waste transfer from sources to waste facilities.

## Slide 11: Pretreatment
Waste Outputs:
Recyclables output
Refuse output
Biomass output
Mass Flow Parameters
distribution of the input biowaste sub-fractions
distribution of macro-impurities between three waste outputs
2nd DECISIVE Webinar: the DST • 11
Notes: Direct emissions and material and energy inputs can be defined either per tonne of input

## Slide 12: Treatment 1/2
AD wet batch & CHP + Composting
(ECO2- organic line )
Material and energy outputs
Biogas generated
Methane yield (%CH4)
Gas Composition
Material Outputs:
Solid refuse
Digestate
Compost
Energy output:
Electricity generated
Direct emissions
N2O, CH4, NH3

## Slide 13: Treatment 2/2
AD wet batch & CHP + Composting
(ECO2- organic line )
Material and energy inputs
Consumption
Water
Electricity
Diesel
Material Outputs:
Solid refuse
Digestate
Compost
Socio-economic aspects
Worker
Public space
Capital goods
Annual Capacity
Lifetime facility
Investment cost

## Slide 14: Transportation II
Truck of 34 t and
velocity: 59 km/h
Material and energy inputs
Amount of trucks/t*km
Diesel consumption
Inventories per tonne*km
Socio-economic aspects
Worker
Public space
Notes: If Pre-treatment and Treatment occur in the same place, as in the case of waste from UAB sent to ECO2, this stage is not necessary and its definition has been skipped. If the Scenario does not include a Pre-treatment phase the Transportation stage is not necessary either, since the Collection phase can be used to bring the waste from the source to the first waste facility (in this case a Treatment facility).

## Slide 15: Bio-based Product use
N2O, CO2 bind
Material and energy inputs
Material and energy outputs
Socio-economic aspects
Agricultural land
N, P, K mineral fertilizer
Diesel consumption
Direct emissions
Use of Compost as fertilizer

## Slide 16: Final disposal
Incineration
Material and energy outputs
Direct emissions
HCl, Dioxins, As, Cd, PB, SO2, NOx, NH3, Hg
Residue outputs
Bottom ash treatment
Fly ash treatment
Energy outputs:
Electricity generated
Heat generated
Material and energy inputs
Diesel Consumption
Socio-economic aspects
Capital goods
Annual Capacity
Lifetime facility
Investment cost

## Slide 17: Bellaterra – Baseline scenario
Summary Baseline scenario definition
Notes: Añadir impr pantaglia

## Slide 18: Bellaterra – Alternative scenario
Summary Alternative scenario definition
Notes: Añadir impr pantaglia

## Slide 19: Scenario assessment results
The radars diagrams only wants to show how the DST works.
Inventories for DECISIVE system are provisional and need to be updated with real data
Notes: Añadir impr pantaglia

## Slide 20: THANK YOU FOR YOUR ATTENTION
Dr. Rosaria Chifari
Fundació ENT
rchifari@ent.cat